## Slide 1: Network-layer Mobility for Linux lispmob.org

## Slide 2
  Why do current IP semantics cause scaling issues?
    Today, “addressing follows topology,” which limits route aggregation compactness
    Overloaded IP address semantic makes efficient routing impossible
    IPv6 does not fix this
“… routing scalability is the most important problem facing the Internet today and must be solved … ”
Internet Architecture Board (IAB)
October 2006 Workshop (RFC 4984)
Notes:   Reduction of routing table size in the “default free zone” (DFZ)
  35,000 active BGP entries
  Why are route scaling issues bad?
    Routers require tons of expensive memory to hold the Internet Routing Table in the forwarding plane
    It’s expensive for network builders/operators
    Replacing equipment for the wrong reason (to hold the routing table); replacement should be to implement new features

## Slide 3: LISP: Introduction
The current IP routing and addressing architecture uses a single numbering space, the IP address, to simultaneously express two functions about a device:
  its identity
  how / where its is attached to the network
The Locator ID Separation Protocol (LISP) creates a new paradigm by splitting
  the device identity, or the endpoint identifier (EID) and
  its location, or its routing locator (RLOC) into two different numbering spaces.
LISP
  requires no hardware / software changes to hosts
  is incrementally deployable in the network infrastructure
  is a simple, open standard protocol (IETF)
Notes: - Reduction of routing table size in the “default free zone” (DFZ)
Incremental introduction of IPv6
Cost-effective multi-homing with potentially no BGP dependency
Ease of renumbering burden when clients change providers
Traffic engineering capabilities, simplify multi-homed routing
Facilitate any-to-any WAN connectivity
Mobility without address changing
virtual machine mobility
reduce operational complexity

## Slide 4: LISP: Overview
LISP creates a Level of indirection with two namespaces: EID and RLOC
EID (Endpoint Identifier) is the IP address of a host – just as it is today
RLOC (Routing Locator) is the IP address of the LISP router for the host
EID-to-RLOC mapping is the distributed architecture that maps EIDs to RLOCs
Network-based solution
No host changes
Minimal configuration
Incrementally deployable
Support for mobility
Address Family agnostic
Prefix Next-hop
w.x.y.1 e.f.g.h
x.y.w.2 e.f.g.h
z.q.r.5 e.f.g.h
z.q.r.5 e.f.g.h
Non-LISP
RLOC Space
EID-to-RLOC mapping
xTR
EID Space
xTR
EID RLOC a.a.a.0/24 w.x.y.1
b.b.b.0/24 x.y.w.2
c.c.c.0/24 z.q.r.5
d.d.0.0/16 z.q.r.5
MS/MR
PxTR
xTR
EID RLOC a.a.a.0/24 w.x.y.1
b.b.b.0/24 x.y.w.2
c.c.c.0/24 z.q.r.5
d.d.0.0/16 z.q.r.5
EID RLOC a.a.a.0/24 w.x.y.1
b.b.b.0/24 x.y.w.2
c.c.c.0/24 z.q.r.5
d.d.0.0/16 z.q.r.5
EID Space

## Slide 5
S1
S2
TR
TR
S
Provider A
10.0.0.0/8
Provider B
11.0.0.0/8
Provider X
12.0.0.0/8
Provider Y
13.0.0.0/8
LISP Site
Mapping System
MR
MS
10.0.0.1
11.0.0.1
13.0.0.2
12.0.0.2
LISP Site
65.1.1.1
Legend:
EIDs -> Green
Locators -> Red
Physical link
12.0.0.2-> 66.2.2.2
LISP Map-Register
(udp 4342)
SHA-1
3.0.0.3/32
12.0.0.2, 13.0.0.2
LISP-MN Control Plane
Map-Registration
PI EID-prefix
2.0.0.0/24
LISP-MN EID
3.0.0.3/32
66.2.2.2

## Slide 6
S1
S2
TR
TR
S
Provider A
10.0.0.0/8
Provider B
11.0.0.0/8
Provider X
12.0.0.0/8
Provider Y
13.0.0.0/8
LISP Site
Mapping System
MR
MS
10.0.0.1
11.0.0.1
13.0.0.2
12.0.0.2
LISP Site
65.1.1.1
Legend:
EIDs -> Green
Locators -> Red
Physical link
LISP-MN Control Plane
Map-Request
PI EID-prefix
2.0.0.0/24
LISP-MN EID
3.0.0.3/32
DNS entry:
D.abc.com A 3.0.0.3
How do I get to 3.0.0.3?
11.0.0.1 -> 3.0.0.3
Map-Request
(udp 4342) nonce
11.0.0.1 -> 65.1.1.1
LISP ECM
(udp 4342)
[1]
[2]
[3]
[4]
11.0.0.1 -> 3.0.0.3
Map-Request
(udp 4342)
nonce
66.2.2.2
2.0.0.2 -> 3.0.0.3

## Slide 7
S1
S2
TR
TR
S
Provider A
10.0.0.0/8
Provider B
11.0.0.0/8
Provider X
12.0.0.0/8
Provider Y
13.0.0.0/8
LISP Site
Mapping System
MR
MS
10.0.0.1
11.0.0.1
13.0.0.2
12.0.0.2
LISP Site
65.1.1.1
Legend:
EIDs -> Green
Locators -> Red
Physical link
LISP-MN Control Plane
Map-Reply
PI EID-prefix
2.0.0.0/24
LISP-MN EID
3.0.0.3/32
66.2.2.2
12.0.0.2 ->11.0.0.1
Map-Reply
(udp 4342)
nonce
3.0.0.3/32
12.0.0.2 [1, 50]
13.0.0.2 [1, 50]
[6]
EID-prefix: 3.0.0.3/32
Locator-set:
12.0.0.2, priority: 1, weight: 50 (D1)
13.0.0.2, priority: 1, weight: 50 (D2)
Mapping
Entry

## Slide 8
S1
S2
TR
TR
S
Provider A
10.0.0.0/8
Provider B
11.0.0.0/8
Provider X
12.0.0.0/8
Provider Y
13.0.0.0/8
LISP Site
Mapping System
MR
MS
10.0.0.1
11.0.0.1
13.0.0.2
12.0.0.2
LISP Site
65.1.1.1
LISP-MN Data Plane
Unicast Packet Forwarding
PI EID-prefix
2.0.0.0/24
LISP-MN EID
3.0.0.3/32
66.2.2.2
This policy controlled
by destination site
DNS entry:
D.abc.com A 3.0.0.3
1
EID-prefix: 3.0.0.3/32
Locator-set:
12.0.0.2, priority: 1, weight: 50 (D1)
13.0.0.2, priority: 1, weight: 50 (D2)
Mapping
Entry
3
2.0.0.2 -> 3.0.0.3
2
2.0.0.2 -> 3.0.0.3
11.0.0.1 -> 12.0.0.2
4
2.0.0.2 -> 3.0.0.3
11.0.0.1 -> 12.0.0.2
7
Legend:
EIDs -> Green
Locators -> Red
Physical link
Notes: TODO: need to reduce the number of details on this slide

## Slide 9
BR
S
Provider B
11.0.0.0/8
Provider X
12.0.0.0/8
Provider Y
13.0.0.0/8
Mapping System
MS
11.0.0.1
13.0.0.2
12.0.0.2
LISP-MN Data Plane
Inter-networking with non-LISP sites
Non-LISP
site
7.0.0.0/24
LISP-MN EID
3.0.0.3/32
PxTR
EID-prefix: 3.0.0.3/32
Locator-set:
12.0.0.2, priority: 1, weight: 50 (D1)
13.0.0.2, priority: 1, weight: 50 (D2)
Mapping
Entry
BGP Announcement: 3.0.0.0/24
Map-Request
Map-Reply
Notes: TODO: need to reduce the number of details on this slide

## Slide 10: LISPmob (lispmob.org)

## Slide 11: LISPmob: Some details
LISPmob is an open-source implementation of LISP-MN
  Linux (kernels 2.6.4 and 3.0.0)
  Compliant with latest draft
  Inter-operability tests with reference LISP implementations (NX-OS, IOS)
LISPmob features
  Mobility
  Multihoming: Multiple interfaces per node
  Full IPv6 support: IPv4-over-IPv6 or IPv6-over-IPv4

## Slide 12: LISPmob: Hardware support
Desktop/Servers
Smartphones
(Android)
Embeded devices
(OpenWRT)